## Slide 1: Comparing Different Results for Force Displacement Graphs

## Slide 2: Comparison Results:
Hoping my results to be in similar range.
Results from a pile dimensions:

## Slide 3: My model dimensions
Axisymetric model, Soil = 100x50x50 m, Pile height = 60m (30m below soil, 30m above soil), Pile diameter = 4m , Wall thickness = 50mm. Based on ‘Siemens Gamesa SG 3.4-132’

## Slide 4: Using STKO Team Recommended Method
Horizontal load applied to surface at top of pile.
Displacement measured at a point on the pile base (in line with soil line)
Reaction force measured from bottom of soil. (Could you try and explain why this works if you are trying to measure the applied lateral force to the top of the pile?)
Notes: very similar to comparison results
DP = Drucker Prager Method for soil
EI = Elastic isotropic for soil
Pile base = point on pile in line with top of soil line

## Slide 5: Using Prescribed Displacement on Control Node
Prescribed displacement applied to control node (point on the top of the pile)
Displacement measured at point on pile base (in line with soil line)
Reaction force taken from the control node.

## Slide 6: Using Prescribed Displacement on surface on the top of the pile.
This time, instead of applying the prescribed displacement to the control node, and measuring the reaction force at the control node, the surface at the top of the pile was used instead and this gave very different results, (not sure why this is). Elastic Isotropic on the left, Drucker Prager on the right.

## Slide 7: Questions
Which is the right way to model the Lateral load applied to the top of the pile vs displacement at base of the pile.
Why can the reaction force be taken at the bottom of the soil, even if you’re trying to measure the lateral load to the top of the pile?
Why are the results all different, if the stiffness, friction parameters etc are all the same. The only thing changing is the applied force vs prescribed displacement and where that is measured.
Why are the results for prescribed displacement so different when measuring control node, vs surface at the top of the pile?